## Slide 1: Toutilo Sound Feedback System
November 2018
Ver. 0.1

## Slide 2: Project Aim
To design and implement a sound feedback system for Toutilo.

## Slide 3: Project Purposes
The purposes of introducing sound as an interaction medium are to reach:
Enhance Operation Safety
Improve Productivity

## Slide 4: Feedback Types
The designed sound feedback can be categorized into two classes:
Operation Confirmation Sound
Notification / Warning Sound

## Slide 5: Operation Confirmation
“User-Driven Feedback”
Audio confirmation will be provided for certain user inputs
for the purpose of acknowledging the successful reception of inputs
usually occurs right after a user input is received

## Slide 6: Operation Confirmation
HMI Code Number | Transition Description
1 | Machine switch on
2 | Machine switch off
3 | Remote controller connected
4 | Remote controller disconnected
5 | Motor power connected
6 | Motor power disconnected
7 | Usage scenario activated

## Slide 7: Notification / Warning Sound
“Machine-driven feedback”
Notification / Warning will be generated actively based on a machine’s perception or its internal states
Normal event notification
Emergency Warning

## Slide 8: Notification / Warning Sound
HMI Code Number | Transition Description
1 | “Idle Mode” Enter
2 | “Idle mode” to “working mode”
3 | “idle mode” to “maneuver mode”
4 | “idle mode” to “autonomous mode”
5 | “working mode” to “idle mode”
6 | “maneuver mode” to “idle mode”
7 | “autonomous mode” to “idle mode”
8 | “working mode” to “autonomous mode”

## Slide 9: Notification / Warning Sound
HMI Code Number | Transition Description
9 | Idle mode duration exceeds xx hours
10 | Abnormal Battery State
11 | Abnormal Left Motor State
12 | Abnormal Right Motor State
13 | Abnormal Leveling Motor State
14 | Abnormal Tool Motor State

## Slide 10: Notification / Warning Sound
HMI Code Number | Transition Description
15 | Approaching the end of field (planned turning point)
16 | Deviating from the planned path
17 | Any other emergency events (?)

## Slide 11: System Architecture Overview (Ver. 1)
(Existing) Toutilo Autonomous Control / Monitor Module
(Existing) Toutilo Manual / Remote Controller
(New) Sound Controller Interface
(New) Toutilo Sound Conductor
(New) Speaker Hardware

## Slide 12: Sound Controller Interface
(Existing) Toutilo Autonomous Control / Monitor Module
(Existing) Toutilo Manual / Remote Controller
(New) Sound Controller Interface
(New) Toutilo Sound Conductor
(New) Speaker Hardware

## Slide 13: Sound Controller Interface
(New) Sound Controller Interface
Build on top of Toutilo’s existing inter-vehicle communication protocol
Using the publisher-subscriber communication paradigm (?)
The interface is defined as a communication channel
All components that need to trigger any sound event publish to this channel
Asynchronous communication

## Slide 14: System Architecture Overview (Ver. 1)
(Existing) Toutilo Autonomous Control / Monitor Module
(Existing) Toutilo Manual / Remote Controller
(New) Sound Controller Interface
(New) Toutilo Sound Conductor
(New) Speaker Hardware

## Slide 15: Toutilo Sound Conductor
(Engineer) Reconfigurable
Using an event-to-sound language to define the sound effect for any event from the interface
Define the duration / loudness / level of importance, etc.
(Finite State) Sound Controller
Coordinated access to the speaker hardware
To address any necessary sound effect overlay
(New) Toutilo Sound Conductor

## Slide 16: System Development Model
(New) Sound Controller Interface
(New) Toutilo Sound Conductor
(New) Speaker Hardware
(Existing) Toutilo Autonomous Control / Monitor Module
(Existing) Toutilo Manual / Remote Controller
Toutilo Hardware
(New) Toutilo Event-Simulator / Generator

## Slide 17: Toutilo Event-Simulator (Generator)
Share the same communication interface as the real Toutilo hardware
Using the same publisher-subscriber communication paradigm
Publish to the same communication channel
Simple user interface to let developers to manually trigger events
(New) Toutilo Event-Simulator / Generator

## Slide 18: System Architecture Overview (Ver. 2)
(Existing) Toutilo Autonomous Control / Monitor Module
(Existing) Toutilo Manual / Remote Controller
(New) Sound Controller Interface
(New) Toutilo Sound Conductor
(New) Speaker Hardware
(New) User / Task Status Monitor

## Slide 19: User / Task Status Monitor
In addition to providing sound feedback based on information collected from the machine, we also want to take “user status” and “task status” into consideration. E.g.
User Fatigue Monitoring
“Sound gamification”
  Incomplete task completion notification or
  positive reward for successful task completion
Extending the Ver 1 design
Requiring additional user / task monitoring capabilities (hardware + Software)
(New) User / Task Status Monitor

## Slide 20: Next Step …
INRIA & Swansea
Agreeing on the overall system design
Agreeing on the Sound Controller Interface
INRIA
Providing sample code for accessing machine information using the Sound Controller Interface
Swansea
Developing Toutilo Sound Conductor
Developing Toutilo Event-Simulator / Generator